## Slide 1: Memory Data Flow ECE/CS 752 Fall 2017
Prof. Mikko H. Lipasti
University of Wisconsin-Madison

## Slide 2: High-IPC Processor

## Slide 3: Memory Data Flow
Memory Data Flow Challenges
  Memory Data Dependences
  Load Bypassing
  Load Forwarding
  Speculative Disambiguation
  The Memory Bottleneck
Cache Hits and Cache Misses
Replacement Policies
Prefetching

## Slide 4: Memory Data Dependences
Besides branches, long memory latencies are one of the biggest performance challenges today.
To preserve sequential (in-order) state in the data caches and external memory (so that recovery from exceptions is possible) stores are performed in order. This takes care of antidependences and output dependences to memory locations.
However, loads can be issued out of order with respect to stores if the out-of-order loads check for data dependences with respect to previous, pending stores.
WAW WAR RAW
store X load X store X
: : :
store X store X load X

## Slide 5: Memory Data Dependences
“Memory Aliasing” = Two memory references involving the same memory location (collision of two memory addresses).
“Memory Disambiguation” = Determining whether two memory references will alias or not (whether there is a dependence or not).
Memory Dependency Detection:
  Must compute effective addresses of both memory references
  Effective addresses can depend on run-time data and other instructions
  Comparison of addresses require much wider comparators
Example code:
  (1) STORE V
  (2) ADD
  (3) LOAD W
  (4) LOAD X
  (5) LOAD V
  (6) ADD
  (7) STORE W
RAW
WAR

## Slide 6: The DAXPY Example
Total Order
Notes: Double-precision A = X plus Y (DAXPY): famous FP kernel for measuring peak FPU throughput and memory bandwidth
Naively: 2 cycle LD, 3 cycle MULTD, 2 cycle ADD, 2 cycle SD: 2 FLOP / 9 cycles = .22 FLOP/cycle; not good enough
Must overlap multiple iterations, issue next loads before previous store completes: load bypassing
Can do it by s/w loop unrolling (requires plenty of architected registers) or let hardware “unroll” the loop with renaming of registers.
Goal: start MULTD and ADDD every cycle (pipelined) to get to 2 FLOP/cycle (10x over naïve baseline).

## Slide 7: Out-of-order Load Issue
Required for high performance
Hardware must monitor prior stores
  No alias: loads free to issue
  Alias: load must honor RAW
Complications
  Large comparators (64-bit addresses)
  Relative order of interleaved stores and loads
    (must forward from most recent prior store)
  Speculative vs. non-speculative load issue

## Slide 8: Optimizing Load/Store Disambiguation
Non-speculative load/store disambiguation
  Loads wait for addresses of all prior stores
  Full address comparison
  Bypass if no match, forward if match
Step (1) can unnecessarily limit performance:
load r5,MEM[r3]  cache miss
store r7, MEM[r5]  RAW for agen, stalled
…
load r8, MEM[r9]  independent load stalled

## Slide 9: Speculative Disambiguation
What if aliases are rare?
  Loads don’t wait for addresses of all prior stores
  Full address comparison of stores that are ready
  Bypass if no match, forward if match
  Check all store addresses when they commit
    No matching loads – speculation was correct
    Matching unbypassed load – incorrect speculation
  Replay starting from incorrect load
Load
Queue
Store
Queue
Load/Store RS
Agen
Reorder Buffer
Mem

## Slide 10: Speculative Disambiguation: Load Bypass
Load
Queue
Store
Queue
Agen
Reorder Buffer
Mem
i1: st R3, MEM[R8]: ??
i2: ld R9, MEM[R4]: ??
i1: st R3, MEM[R8]: x800A
i2: ld R9, MEM[R4]: x400A
i1 and i2 issue in program order
i2 checks store queue (no match)

## Slide 11: Speculative Disambiguation: Load Forward
Load
Queue
Store
Queue
Agen
Reorder Buffer
Mem
i1: st R3, MEM[R8]: ??
i2: ld R9, MEM[R4]: ??
i1: st R3, MEM[R8]: x800A
i2: ld R9, MEM[R4]: x800A
i1 and i2 issue in program order
i2 checks store queue (match=>forward)

## Slide 12: Speculative Disambiguation: Safe Speculation
Load
Queue
Store
Queue
Agen
Reorder Buffer
Mem
i1: st R3, MEM[R8]: ??
i2: ld R9, MEM[R4]: ??
i1: st R3, MEM[R8]: x800A
i2: ld R9, MEM[R4]: x400C
i1 and i2 issue out of program order
i1 checks load queue at commit (no match)

## Slide 13: Speculative Disambiguation: Violation
Load
Queue
Store
Queue
Agen
Reorder Buffer
Mem
i1: st R3, MEM[R8]: ??
i2: ld R9, MEM[R4]: ??
i1: st R3, MEM[R8]: x800A
i2: ld R9, MEM[R4]: x800A
i1 and i2 issue out of program order
i1 checks load queue at commit (match)
  i2 marked for replay

## Slide 14: Use of Prediction
If aliases are rare: static prediction
  Predict no alias every time
    Why even implement forwarding? PowerPC 620 doesn’t
  Pay misprediction penalty rarely
If aliases are more frequent: dynamic prediction
  Use PHT-like history table for loads
    If alias predicted: delay load
    If aliased pair predicted: forward from store to load
      More difficult to predict pair [store sets, Alpha 21264]
  Pay misprediction penalty rarely
Memory cloaking [Moshovos, Sohi, ISCA 1997]
  Predict load/store pair
  Directly copy store data register to load target register
  Reduce data transfer latency to absolute minimum

## Slide 15: Load/Store Disambiguation Discussion
RISC ISA:
  Many registers, most variables allocated to registers
  Aliases are rare
  Most important to not delay loads (bypass)
  Alias predictor may/may not be necessary
CISC ISA:
  Few registers, many operands from memory
  Aliases much more common, forwarding necessary
  Incorrect load speculation should be avoided
  If load speculation allowed, predictor probably necessary
Address translation:
  Can’t use virtual address (must use physical)
  Wait till after TLB lookup is done
  Or, use subset of untranslated bits (page offset)
    Safe for proving inequality (bypassing OK)
    Not sufficient for showing equality (forwarding not OK)

## Slide 16: Store Queue Implementation
Store color assigned at dispatch, increases monotonically
Load inherits color from preceding store, only forwards if store is older
Priority logic must find nearest matching store
Address
Color
?=
Address
Data
≤
Store Color
Priority Logic
Load Addr
Load Color
Forwarded Data
Load Color

## Slide 17: Store Queue Complications
If entries are positional, priority logic looks like carry chain (slow)
If entries are not positional, priority logic is quite complex
  See [Buyuktosunogly, El-Moursy, Albonesi, 2002 IEEE ASIC/SOC Conference]
Partial store/load overlap may prevent bypassing (not all bytes present)
  Must stall load instead
Store color has finite range, clever logic trick:
  For 2n store queue entries, use (n+1) bits for color, e.g. 16 SQ entries requires 5 bits
  If leading bit of oldest store is zero, use unsigned comparisons
  If leading bit of oldest store is one, use signed comparisons
Address
Color
?=
Tag
Data
≤
Color
Priority Logic
Load Addr
Load Color
ForwardedData

## Slide 18: The Memory Bottleneck

## Slide 19: Load/Store Processing
For both Loads and Stores:
  Effective Address Generation:
    Must wait on register value
    Must perform address calculation
  Address Translation:
    Must access TLB
    Can potentially induce a page fault (exception)
For Loads: D-cache Access (Read)
    Can potentially induce a D-cache miss
    Check aliasing against store buffer for possible load forwarding
    If bypassing store, must be flagged as “speculative” load until completion
For Stores: D-cache Access (Write)
    When completing must check aliasing against “speculative” loads
    After completion, wait in store buffer for access to D-cache
    Can potentially induce a D-cache miss

## Slide 20: Easing The Memory Bottleneck
Notes: 2 changes:
multiple L/S units (later)
missed load buffer (MSHR) for nonblocking cache

## Slide 21: Superscalar Caches
Increasing issue width => wider caches
Parallel cache accesses are harder than parallel functional units
Fundamental difference:
  Caches have state, functional units don’t
  Operation thru one port affects future operations thru others
Several approaches used
  True multi-porting
  Multiple cache copies
  Virtual multi-porting
  Multi-banking (interleaving)

## Slide 22: True Multiporting of SRAM
“Word” Lines
-select a row
“Bit” Lines
-carry data in/out

## Slide 23: True Multiporting of SRAM
Would be ideal
Increases cache area
  Array becomes wire-dominated
Slower access
  Wire delay across larger area
  Cross-coupling capacitance between wires
Read stability suffers if latch drives bitline
  Need isolating access logic (2T per bitline)

## Slide 24: Multiple Cache Copies
Used in DEC Alpha 21164, IBM Power4
Independent load paths
Single shared store path
  May be exclusive with loads, or internally dual-ported
Bottleneck, not practically scalable beyond 2 paths
Provides some fault-tolerance
  Parity protection per copy
  Parity error: restore from known-good copy
  Avoids more complex ECC (no RMW for subword writes), still provides SEC
Load Port 0
Load Port 1
Store Port

## Slide 25: Virtual Multiporting
Used in IBM Power2 and DEC 21264
  Wave pipelining: pipeline wires WITHOUT latches
Time-share a single port
Not scalable beyond 2 ports
Requires very careful array design to guarantee balanced paths
  Second access cannot catch up with first access
Short path constraint limits maximum clock period
  Does not support CPU power states
Port 0
Port 1

## Slide 26: Multi-banking or Interleaving
Used in Intel Pentium (8 banks)
Need routing network
Must deal with bank conflicts
  Bank conflicts not known till address generated
  Difficult in non-data-capture machine with speculative scheduling
    Replay – looks just like a cache miss
  Sensitive to bank interleave: fine-grained vs. coarse-grained
Port 0
Port 1
Bank 0
Crossbar
Crossbar
Port 0
Port 1
Bank 1
Bank 2
Bank 3
Bank 4
Bank 5
Bank 6
Bank 7

## Slide 27: Memory Data Flow
Memory Data Flow Challenges
  Memory Data Dependences
  Load Bypassing
  Load Forwarding
  Speculative Disambiguation
  The Memory Bottleneck
Cache Hits and Cache Misses
Replacement Policies
Prefetching

## Slide 28: Caches and Performance
Caches
  Enable design for common case: cache hit
    Cycle time, pipeline organization
    Recovery policy
  Uncommon case: cache miss
    Fetch from next level
      Apply recursively if multiple levels
    What to do in the meantime?
What is performance impact?
Various optimizations are possible

## Slide 29: Performance Impact
Cache hit latency
  Included in “pipeline” portion of CPI
  Typically 1-3 cycles for L1 cache
    Intel/HP McKinley: 1 cycle
      Heroic physical design of cache arrays, peripheral logic
      Only register indirect addressing supported: load r1, (r2)
    IBM Power4: 3 cycles
      Address generation
      Array access
      Word select and align
      Register file write (no bypass)

## Slide 30: Cache Hit continued
Cycle stealing common
  Address generation < cycle
  Array access > cycle
  Clean, FSD cycle boundaries violated
Speculation rampant
  “Predict” cache hit
  Don’t wait for (full) tag check
  Consume fetched word in pipeline
  Recover/flush when miss is detected
    Reportedly 7 cycles later in Intel Pentium 4
AGEN
CACHE
AGEN
CACHE

## Slide 31: Cache Hits and Performance
Cache hit latency determined by:
  Cache organization
    Associativity
      Parallel tag checks expensive, slow
      Way select slow (fan-in, wires)
    Block size
      Word select may be slow (fan-in, wires)
    Number of block (sets x associativity)
      Wire delay across array
      “Manhattan distance” = width + height
      Word line delay: width
      Bit line delay: height
Array design is an art form
  Detailed analog circuit/wire delay modeling
  DRC “flexibility”
Word Line
Bit Line

## Slide 32: Cache Misses and Performance
Miss penalty
  Detect miss: 1 or more cycles
  Find victim (replace block): 1 or more cycles
    Write back if dirty
  Request block from next level: several cycles
    May need to find line from one of many caches (coherence)
  Transfer block from next level: several cycles
    (block size) / (bus width)
  Fill block into data array, update tag array: 1+ cycles
  Resume execution
In practice: 6 cycles to 100s of cycles

## Slide 33: Cache Miss Rate
Determined by:
  Program characteristics
    Temporal locality
    Spatial locality
  Cache organization
    Block size, associativity, number of sets
    Replacement policy

## Slide 34: Review: Placement
Address Range
  Exceeds cache capacity
Map address to finite capacity
  Called a hash
  Usually just masks high-order bits
Direct-mapped
  Block can only exist in one location
  Hash collisions cause problems
Hash
Address
Index
Data Out
Index
Offset
32-bit Address
Offset
Block Size

## Slide 35: Review: Identification
Fully-associative
  Block can exist anywhere
  No more hash collisions
Identification
  How do I know I have the right block?
  Called a tag check
    Must store address tags
    Compare against address
Expensive!
  Tag & comparator per block
Hash
Address
Data Out
Offset
32-bit Address
Offset
Tag
Hit
Tag Check
?=
Tag

## Slide 36: Review: Placement
Set-associative
  Block can be in a locations
  Hash collisions:
    a still OK
Identification
  Still perform tag check
  However, only a in parallel
Hash
Address
Data Out
Offset
Index
Offset
32-bit Address
Tag
Index
a Tags
a Data Blocks
Index
?=
?=
?=
?=
Tag

## Slide 37: Memory Data Flow
Memory Data Flow Challenges
  Memory Data Dependences
  Load Bypassing
  Load Forwarding
  Speculative Disambiguation
  The Memory Bottleneck
Cache Hits and Cache Misses
Replacement Policies
Prefetching

## Slide 38: Replacement
Cache has finite size
  What do we do when it is full?
Analogy: desktop full?
  Move books to bookshelf to make room
  Bookshelf full? Move least-used to library
  Etc.
Same idea:
  Move blocks to next level of cache

## Slide 39: Replacement
How do we choose victim?
  Verbs: Victimize, evict, replace, cast out
Many policies are possible
  FIFO (first-in-first-out)
  LRU (least recently used), pseudo-LRU
  LFU (least frequently used)
  NMRU (not most recently used)
  NRU
  Pseudo-random (yes, really!)
  Optimal
  Etc

## Slide 40: Optimal Replacement Policy?
[Belady, IBM Systems Journal, 1966]
Evict block with longest reuse distance
  i.e. next reference to block is farthest in future
  Requires knowledge of the future!
Can’t build it, but can model it with trace
  Process trace in reverse
  [Sugumar&Abraham] describe how to do this in one pass over the trace with some lookahead (Cheetah simulator)
Useful, since it reveals opportunity
  (X,A,B,C,D,X): LRU 4-way SA $, 2nd X will miss
  See [Jimenez MICRO ‘13]

## Slide 41: Least-Recently Used
For a=2, LRU is equivalent to NMRU
  Single bit per set indicates LRU/MRU
  Set/clear on each access
For a>2, LRU is difficult/expensive
  Timestamps? How many bits?
    Must find min timestamp on each eviction
  Sorted list? Re-sort on every access?
List overhead: log2(a) bits /block
  Shift register implementation

## Slide 42: Practical Pseudo-LRU
Rather than true LRU, use binary tree
Each node records which half is older/newer
Update nodes on each reference
Follow older pointers to find LRU victim
0
0
1
0
1
1
1
J
F
C
B
X
Y
A
Z
Older
Newer

## Slide 43: Practical Pseudo-LRU In Action
J
F
C
B
X
Y
A
Z
J
Y
X
Z
B
C
F
A
011: PLRU Block B is here
110: MRU block is here
Z < A
Y < X
B < C
J < F
A > X
C < F
A > F
B | C | F | A
 | J |  | 
 | Y | X | 
 |  | Z | 
Partial Order Encoded in Tree:

## Slide 44: Practical Pseudo-LRU
Binary tree encodes PLRU partial order
  At each level point to LRU half of subtree
Each access: flip nodes along path to block
Eviction: follow LRU path
Overhead: (a-1)/a bits per block
Recently revisited [Jimenez MICRO-2013]
0
0
1
0
1
1
1
J
F
C
B
X
Y
A
Z
011: PLRU Block B is here
110: MRU block is here
Older
Newer
Refs: J,Y,X,Z,B,C,F,A

## Slide 45: True LRU Shortcomings
Streaming data/scans: x0, x1, …, xn
  Effectively no temporal reuse
Thrashing: reuse distance > a
  Temporal reuse exists but LRU fails
All blocks march from MRU to LRU
  Other conflicting blocks are pushed out
For n>a no blocks remain after scan/thrash
  Incur many conflict misses after scan ends
Pseudo-LRU sometimes helps a little bit

## Slide 46: Segmented or Protected LRU
[I/O: Karedla, Love, Wherry, IEEE Computer 27(3), 1994]
[Cache: Wilkerson, Wade, US Patent 6393525, 1999]
Partition LRU list into filter and reuse lists
On insert, block goes into filter list
On reuse (hit), block promoted into reuse list
Provides scan & some thrash resistance
  Blocks without reuse get evicted quickly
  Blocks with reuse are protected from scan/thrash blocks
No storage overhead, but LRU update slightly more complicated

## Slide 47: Protected LRU: LIP
Simplified variant of this idea: LIP
  Qureshi et al. ISCA 2007
Insert new blocks into LRU position, not MRU position
  Filter list of size 1, reuse list of size (a-1)
Do this adaptively: DIP
Use set dueling to decide LIP vs. LRU
  1 (or a few) set uses LIP vs. 1 that uses LRU
  Compare hit rate for sets
  Set policy for all other sets to match best set

## Slide 48: Not Recently Used (NRU)
Keep NRU state in 1 bit/block
  Bit is set to 0 when installed (assume reuse)
  Bit is set to 0 when referenced (reuse observed)
  Evictions favor NRU=1 blocks
  If all blocks are NRU=0
    Eviction forces all blocks in set to NRU=1
    Picks one as victim (can be pseudo-random, or rotating, or fixed left-to-right)
Simple, similar to virtual memory clock algorithm
Provides some scan and thrash resistance
  Relies on “randomizing” evictions rather than strict LRU order
Used by Intel Itanium, Sparc T2

## Slide 49: RRIP [Jaleel et al. ISCA 2010]
Re-reference Interval Prediction
Extends NRU to multiple bits
  Start in the middle, promote on hit, demote over time
Can predict near-immediate, intermediate, and distant re-reference
Low overhead: 2 bits/block
Static and dynamic variants (like LIP/DIP)
  Set dueling

## Slide 50: Least Frequently Used
Counter per block, incremented on reference
Evictions choose lowest count
  Logic not trivial (a2 comparison/sort)
Storage overhead
  1 bit per block: same as NRU
  How many bits are helpful?

## Slide 51: Cache Replacement Championship
CRC-1 Held at ISCA 2010
  http://www.jilp.org/jwac-1
  Several variants, improvements
  Simulation infrastructure
    Implementations for all entries
CRC-2 held at ISCA 2017
  http://crc2.ece.tamu.edu
  Several categories, each with different winner
  Overall winner: Hawkeye (but close)

## Slide 52: Hawkeye Replacement
Based on Belady’s OPT algorithm
  Observe from the past
  Train predictor
  Apply predictor to present
[Jain, Lin, CRC-2]

## Slide 53: Replacement Recap
Replacement policies affect capacity and conflict misses
Policies covered:
  Belady’s optimal replacement
  Least-recently used (LRU)
  Practical pseudo-LRU (tree LRU)
  Protected LRU
    LIP/DIP variant
    Set dueling to dynamically select policy
  Not-recently-used (NRU) or clock algorithm
  RRIP (re-reference interval prediction)
  Least frequently used (LFU)
Championship contests

## Slide 54: Replacement References
S. Bansal and D. S. Modha. “CAR: Clock with Adaptive Replacement”, In FAST, 2004.
A. Basu et al. “Scavenger: A New Last Level Cache Architecture with Global Block Priority”. In Micro-40, 2007.
L. A. Belady. A study of replacement algorithms for a virtual-storage computer. In IBM Systems journal, pages 78–101, 1966.
M. Chaudhuri. “Pseudo-LIFO: The Foundation of a New Family of Replacement Policies for Last-level Caches”. In Micro, 2009.
F. J. Corbat´o, “A paging experiment with the multics system,” In Honor of P. M. Morse, pp. 217–228, MIT Press, 1969.
A. Jaleel, et al. “Adaptive Insertion Policies for Managing Shared Caches”. In PACT, 2008.
Aamer Jaleel, Kevin B. Theobald, Simon C. Steely Jr. , Joel Emer, “High Performance Cache Replacement Using Re-Reference Interval Prediction “, In ISCA, 2010.
S. Jiang and X. Zhang, “LIRS: An efficient low inter-reference recency set replacement policy to improve buffer cache performance,” in Proc. ACM SIGMETRICS Conf., 2002.
T. Johnson and D. Shasha, “2Q: A low overhead high performance buffer management replacement algorithm,” in VLDB Conf., 1994.
S. Kaxiras et al. Cache decay: exploiting generational behavior to reduce cache leakage power. In ISCA-28, 2001.
A. Lai, C. Fide, and B. Falsafi. Dead-block prediction & dead-block correlating prefetchers. In ISCA-28, 2001
D. Lee et al. “LRFU: A spectrum of policies that subsumes the least recently used and least frequently used policies,” IEEE Trans.Computers, vol. 50, no. 12, pp. 1352–1360, 2001.

## Slide 55: Replacement References
W. Lin et al. “Predicting last-touch references under optimal replacement.” Technical Report CSE-TR-447-02, U. of Michigan, 2002.
H. Liu et al. “Cache Bursts: A New Approach for Eliminating Dead Blocks and Increasing Cache Efficiency.” In Micro-41, 2008.
G. Loh. “Extending the Effectiveness of 3D-Stacked DRAM Caches with an Adaptive Multi-Queue Policy”. In Micro, 2009.
C.-K. Luk et al. Pin: building customized program analysis tools with dynamic instrumentation. In PLDI, pages 190–200, 2005.
N. Megiddo and D. S. Modha, “ARC: A self-tuning, low overhead replacement cache,” in FAST, 2003.
E. J. O’Neil et al. “The LRU-K page replacement algorithm for database disk buffering,” in Proc. ACM SIGMOD Conf., pp. 297–306, 1993.
M. Qureshi, A. Jaleel, Y. Patt, S. Steely, J. Emer. “Adaptive Insertion Policies for High Performance Caching”. In ISCA-34, 2007.
K. Rajan and G. Ramaswamy. “Emulating Optimal Replacement with a Shepherd Cache”. In Micro-40, 2007.
J. T. Robinson and M. V. Devarakonda, “Data cache management using frequency-based replacement,” in SIGMETRICS Conf, 1990.
R. Sugumar and S. Abraham, “Efficient simulation of caches under optimal replacement with applications to miss characterization,” in SIGMETRICS, 1993.
Y. Xie, G. Loh. “PIPP: Promotion/Insertion Pseudo-Partitioning of Multi-Core Shared Caches.” In ISCA-36, 2009
Y. Zhou and J. F. Philbin, “The multi-queue replacement algorithm for second level buffer caches,” in USENIX Annual Tech. Conf, 2001.

## Slide 56: Memory Data Flow
Memory Data Flow Challenges
  Memory Data Dependences
  Load Bypassing
  Load Forwarding
  Speculative Disambiguation
  The Memory Bottleneck
Cache Hits and Cache Misses
Replacement Policies
Prefetching

## Slide 57: Prefetching
Even “demand fetching” prefetches other words in block
  Spatial locality
Prefetching is useless
  Unless a prefetch costs less than demand miss
Ideally, prefetches should
  Always get data before it is referenced
  Never get data not used
  Never prematurely replace data
  Never interfere with other cache activity

## Slide 58: Software Prefetching
For example:
do j= 1, cols
do ii = 1 to rows by BLOCK
prefetch (&(x[ii,j])+BLOCK) # prefetch one block ahead
do i = ii to ii + BLOCK-1
sum = sum + x[i,j]
How many blocks ahead should we prefetch?
  Affects timeliness of prefetches
  Must be scaled based on miss latency

## Slide 59: Hardware Prefetching
What to prefetch
  One block spatially ahead
  N blocks spatially ahead
  Based on observed stride, track/prefetch multiple strides
Training hardware prefetcher
  On every reference (expensive)
  On every miss (information loss)
  Misses at what level of cache?
  Prefetchers at every level of cache?
Pressure for nonblocking miss support (MSHRs)

## Slide 60: Prefetching for Pointer-based Data Structures
What to prefetch?
  Next level of tree: n+1, n+2, n+?
    Entire tree? Or just one path
  Next node in linked list: n+1, n+2, n+?
Jump-pointer prefetching [Roth, Sohi, ISCA 1999]
  Software places jump pointers in data structure
Content-driven data prefetching [Cooksey et al. ASPLOS 2002]
  Hardware scans blocks for pointers
0xafde
0xfde0
0xde04

## Slide 61: Stream or Prefetch Buffers
Prefetching causes capacity and conflict misses (pollution)
  Can displace useful blocks
Aimed at compulsory and capacity misses
Prefetch into buffers, NOT into cache
  On miss start filling stream buffer with successive lines
  Check both cache and stream buffer
    Hit in stream buffer => move line into cache (promote)
    Miss in both => clear and refill stream buffer
Performance
  Very effective for I-caches, less for D-caches
  Multiple buffers to capture multiple streams (better for D-caches)
Can use with any prefetching scheme to avoid pollution

## Slide 62: Case Study: Global History Buffer
[K. Nesbit, J. Smith, “Prefetching using a global history buffer”, HPCA 2004]
  Following slides © K. Nesbit, J. Smith
Hardware prefetching scheme
Monitors miss stream
Learns correlations
Issues prefetches for likely next address

## Slide 63: Markov Prefetching
Markov prefetching forms address correlations
  Joseph and Grunwald (ISCA ‘97)
Uses global memory addresses as states in the Markov graph
Correlation Table approximates Markov graph
B
C
B
A
B
C
Correlation Table
1st predict.
2nd predict.
miss
address
A B C A B C B C . . .
A
B
C
1
.5
Miss Address Stream
1
.5
Markov Graph
A

## Slide 64: Correlation Prefetching
Distance Prefetching forms delta correlations
  Kandiraju and Sivasubramaniam (ISCA ‘02)
Delta-based prefetching leads to much smaller table than “classical” Markov Prefetching
Delta-based prefetching can remove compulsory misses
Markov Prefetching
1 1 -2 1 1 -1 1
Global Delta Stream
Distance Prefetching
27 28 29 27 28 29 28 29
Miss Address Stream
1
1
-1
-2
-2
-1
1
global
delta
28
29
28
29
27
28
29
1st predict.
2nd predict.
miss
address
1st predict.
2nd predict.

## Slide 65: Global History Buffer (GHB)
Holds miss address history in FIFO order
Linked lists within GHB connect related addresses
  Same static load
  Same global miss address
  Same global delta
Global History Buffer
miss addresses
Index Table
FI
Load PC
Linked list walk is short compared with L2 miss latency
FO

## Slide 66: GHB - Example
Miss Address Stream
Global History Buffer
miss address
pointer
pointer
Index Table
28
29
29
29
head pointer
28
27
27
27 28 29 27 28 29 28
27
=> Current
=> Prefetches
Key
28
29
28
29
Global Miss
Address
Notes: Change addresses to be consistent – make numbers larger, darker

## Slide 67: GHB – Deltas
1
4
8
1 8 8 1 4 4 1 8 8
Global Delta Stream
Miss Address Stream
27 28 36 44 45 49 53 54 62 70
71
1
1
8
=> Current
=> Prefetches
Key
8
4
4
Width
Depth
Hybrid
Markov Graph
.3
.3
.3
.7
.7
.7
71 + 8 => 79
79 + 8 => 87
Prefetches
71 + 4 => 75
79 + 4 => 79
Prefetches
71 + 8 => 79
71 + 4 => 75
Prefetches
Notes: Add absolute prefetch addresses

## Slide 68: GHB – Hybrid Delta
Width prefetching suffers from poor accuracy and short look-ahead
Depth prefetching has good look-ahead, but may miss prefetch opportunities when a number of “next” addresses have similar probability
The hybrid method combines depth and width

## Slide 69: GHB - Hybrid Example
79 + 4 => 79
71 + 4 => 75
Global History Buffer
miss address
pointer
pointer
Index Table
head pointer
27
28
36
44
45
49
53
1
1
=> Current
=> Prefetches
Key
54
62
70
4
8
8
8
Global
Delta
1 8 8 1 4 4 1 8 8
Global Delta Stream
Miss Address Stream
27 28 36 44 45 49 53 54 62 70
71
1
8
4
4
71
8
71 + 8 => 79
79 + 8 => 87
Prefetches

## Slide 70: Prefetching Championships
DPC-1 held at HPCA 2009
  http://www.jilp.org/dpc
  Winner: AMPM prefetching
    Robust to out-of-order issue by capturing patterns instead of strides
DPC-2 held at ISCA 2015
  http://comparch-conf.gatech.edu/dpc2
  Winner: Best-offset prefetcher
    Based on ideas from Sandbox Prefetcher [Pugsley et al. HPCA 2014]
    Considers prefetch timeliness
Simulation infrastructure
  Implementations for all entries

## Slide 71: Prefetching Recap
Prefetching anticipates future memory references
  Software prefetching
  Next-block, stride prefetching
  Global history buffer prefetching
Issues/challenges
  Accuracy
  Timeliness
  Overhead (bandwidth)
  Conflicts (displace useful data)

## Slide 72: Summary
Memory Data Flow
  Memory Data Dependences
  Load Bypassing
  Load Forwarding
  Speculative Disambiguation
  The Memory Bottleneck
Cache Hits and Cache Misses
Replacement Policies
Prefetching